FLOWERS FOR THE LITTLE MERMAID

We all know that generating electricity with wind does not produce toxic gases, pollutes the environment and does not contribute to the greenhouse effect.

But inevitably produces a visual impact, which is why we thought to make a sculptural treatment of the apparatus, which added to the features in location, we conducted a project called Flowers for Little Mermaid.

This project is a public square of eight multicolored large flowers, sloping gracefully as touching the water with their petals turning with the wind.

Data for each wind generator.

Rated Power: 150kW

Rotor diameter : 32 m

Blade length : 16 m

Paddle Weight : 1.35 Tons

Weight: 12.5 Tonnes

Voltage : 400 V

Rated Frequency: 50 Hz

Height: 21 m

Control system: Stall

This system, according to the operating curve and having the wind characteristics at the site, the order can generate 700 MWh per year per wind turbine.