PODIUM

REFSHALEØEN \ COPENHAGEN \ DENMARK

2014 LAGI Competition Proposal

PODIUM is a gathering of sustainable activities. It is a platform for sharing knowledge and discussing possible solutions to our climate problems. We believe that the way to approach these problems is by creating a space for debate and awareness where people together can find the solutions.

This proposal aims to change peoples behaviour and attitude to how we act according to our climate. This is the key factor in changing our climate problems. We need to learn how to make the right decisions and take responsibility of our actions and choices. The best way of learning is through others and learning from their experiences. It is important to realize that everyday we are making decisions that are affecting the climate. PODIUM is about sharing these ideas and suggestions for how to make the right choices, which will help our climate getting cleaner.

PODIUM materials

The construction is made from eight shipping containers, with both sitting places, working spaces and urban gardening. The containers will invite for different activities, which could involve conferences, lectures, workshops, discussions and gardening classes.

Each container measure 6m x 2,5m x 2,5m, this means that each container is 15m2. In total that is 120m2 of space, with the possibility of adding more containers to the construction, adapting to the needs.

On top of the construction, 26 m2 of solar panels are placed; these will supply energy for the construction. According to the electricity need, more solar panels can be added if needed.

The reason for using solar energy is that it’s a natural clean energy source produced by the sun. A solar panel electricity system captures the sun's energy using photovoltaic cells. These cells don't need direct sunlight to work; they can still generate some electricity on a cloudy day. In Denmark the average energy production is 1000 kWh pr. m2 pr. year on a horizontal surface. To optimize the production the panels should have an angle of 45( and be facing south, then it can produce 1250 kWh pr. m2 pr. year. If we use solar panels with an efficiency of 10% the energy production pr. m2 will be 125 kWh pr. m2. The 26 solar panels on the construction will then produce 3250 kWh pr. year. The energy consumption of an average house of 4 people is 4000 kWh pr. year and we therefore believe that 26 panels are enough for this construction.

The excess of the energy will be stored in batteries and it will be available for use when there is a need for it.

PODIUM history

The old shipyard at Refshaleøen has been an important background for this proposal, and since this has been defining the area for a long period of time, it should be an important factor in the new definition of the area. The construction is therefore visualizing the link to the old shipyard by using shipping containers and implementing windows and fences inspired by ships.

The construction will be visible from the other side of the canal, and will be a new symbol for Refshaleøen, defining the area as centre for sustainability. The construction has a clear link to the old shipyard industry, and is using the old identity of the area as a solid foundation for building a new identity centred on sustainability.

PODIUM impact

The proposal will give the opportunity for people to discuss the climate problems in order to find solutions and to create awareness. By sharing ideas and gathering people in one place, it is possible to get attention and influence on a bigger scale. It is also important to indicate that everyone can make a difference every day, by making small changes in his or her everyday life. By creating awareness of the problems and encouraging people to find solutions, it is possible to expand the concept of sustainability.